## Slide 1
ORC Turbomachinery –
from the cycle to the blade design
Fundamentals lecture + hands-on Python tutorial
+
Specific aspects of small-scale ORC turbines
First KCORC Summer School on innovative ORC and heat pump technologies
Jan Špale, PhD. | CTU in Prague | TUM Garching | 8 September 2026
Notes: Open with the end-to-end challenge: cycle boundary conditions are easy; designing a fixed, supersonic, real-fluid turbine stage is not. The notebook and slides alternate throughout the session. [Sources] - KCORC_SummerSchool_updated.pdf — event title, scope and modeling-workshop context. - User brief — session date, duration and audience. - PhD_Thesis_JS_15122024_final.pdf — Chapter 4 design methodology. [/Sources]

## Slide 2
TEACHING ROUTE
Understand the machine first, then we open Python… after coffee
KCORC 2026 | CTU UCEEB
01 Foundations
- turbine-cycle coupling
- Blade rows and velocity triangles
- Real-fluid nozzle physics
02 Short break
Close the lecture.
Open JupyterLab.
Work in pairs.
03 Engineering experiment
Predict a change.
Run a calculation.
Explain the result.

## Slide 3
CYCLE AND MACHINE
The turbine is part of a closed thermodynamic loop
F03
Spale, PhD thesis (2024); original teaching diagrams
KCORC 2026 | CTU UCEEB
HEATER / EVAPORATOR
TURBINE
CONDENSER
P
Heat in
Generator
Heat rejected
Liquid
High-pressure vapour
Low-pressure vapour
Not just an efficiency box
Its flow capacity, exit state and speed constraints feed back into the cycle.
Notes: Start from the familiar four-component ORC. The pump raises the pressure of a liquid; the turbine extracts shaft work from a vapour. Recuperation is intentionally omitted from the drawing. Point out that the turbine outlet state sets condenser duty and whether recuperation is possible. The pressure levels belong to a coupled network, not to an isolated prescribed turbine alone. Diagram is an original simplified teaching schematic. Suggested pace: ~2 min. [Sources] AUTHOR-SUPPLIED: Jan Spale, PhD thesis, PhD_Thesis_JS_15122024_final.pdf (2024), Chapters 2 and 4; use printed page numbers where specified. AUTHOR-SUPPLIED VISUAL ASSETS: UCEEB_prezentace_vzor_022026_CZ.pptx. Original UCEEB logos and cover background reused; Arial is the available sans-serif substitute for Technika. [/Sources]

## Slide 4
CYCLE AND MACHINE
Cycle and turbine must be designed in both directions
F04
KCORC 2026 | CTU UCEEB
CYCLE → TURBINE
Fluid and inlet total state
Outlet static pressure
Design mass flow
Heat source variability
TURBINE → CYCLE
Swallowing capacity
Efficiency and outlet enthalpy
Speed / torque operating range
Leakage, losses
Notes: Distinguish boundary conditions in a design exercise from unknowns in an operating cycle. With a fixed choked stator, the inlet thermodynamic state and throat area constrain mass flow. In sliding-pressure operation the cycle energy balance and turbine capacity jointly determine pressure and flow. A valve can separate evaporator pressure from turbine inlet pressure, but does not remove the turbine capacity equation. Inlet pressures and enthalpies for choking should be total quantities, or use negligible approach kinetic energy as an explicit assumption.

## Slide 5
CYCLE AND MACHINE
… not all turbine powers are the same
F05
KCORC 2026 | CTU UCEEB
Aerodynamic power
Change in fluid
angular momentum
Shaft power
After the mechanical losses are included in the model
Net electrical power
After generator, converter,
- At the el. outlet, after all aux. are considered

## Slide 6
ECONOMICS AND SCALE
Engineer‘s goal for an ORC turbine:
Optimise useful annual energy yield within an affordable machine
F06
KCORC 2026 | CTU UCEEB
Peak isentropic efficiency
does not always make the best business case.
Few parts and repeatable manufacture
Reliable operation across variable heat source
Low leakage and manageable maintenance
what extra annual value pays for the extra aerodynamic complexity?...
Notes: Frame this as an engineering objective rather than a claim that efficiency does not matter in ORC. Heat-source intermittency, small product volumes, service costs and total installed cost can make a simpler stage commercially attractive. A two-stage or more elaborate design remains justified where its extra annual electricity and availability outweigh its added cost. For discussion, compare a slightly less efficient but robust machine with a narrow high-efficiency design that spends much of the year away from its optimum.

## Slide 7
WHY ORC IS DIFFERENT
Molecular mass and complexity change the velocity scale
F07
KCORC 2026 | CTU UCEEB
Molecular mass
Larger molar mass M means a smaller gas constant per unit mass.
Molecular complexity
Internal degrees of freedom
change heat capacities
and the ratio cp/cv.
Often smaller specific „head“ (enthalpy drop) and speed of sound.
Notes: Source-derived: the thesis section 2.3 discusses molar mass, molecular degrees of freedom and sound speed in a polytropic ideal-gas illustration. Qualification added for teaching: mass and complexity are related in many organic fluids but are not the same variable. The ideal-gas equations on this slide are intuition, not the real-fluid property model. At equal T0, pressure ratio and gamma, ideal-gas specific head scales with R_s and therefore with inverse molar mass. At changing gamma, inlet conditions or near saturation this is not a universal proportionality. Dense-vapour expansion must be evaluated with a real EOS.

## Slide 8
WHY ORC IS DIFFERENT
Even a small enthalpy drop often leads to supersonic designs
F08
KCORC 2026 | CTU UCEEB
Pressure ratio
4.00
p0 / p2
Volume-flow ratio
4.40
rho0 / rho2,is
Specific head
28.8 kJ/kg
h0 - h2,is
This is for HFO R-1233zdE… do you know typical steam turbine specific heads? And pressure ratios?

## Slide 9
WHY ORC IS DIFFERENT
ORC is not just a small steam turbine with a different fluid name
F09
KCORC 2026 | CTU UCEEB
Shared physics
Mass, momentum and energy conservation; rotor Euler work; viscous losses.
Head per stage
Organic fluids often allow few stages the loading and speed limits still decide.
Expansion path
Steam may become wet. ORC fluids may be dry, wet or near-isentropic. Check the path! (although most are usually dry)
Thermodynamic model
Steam also needs real fluid properties. A constant gamma baseline is not universal…
Notes: Avoid treating all steam turbines as ideal-gas machines or all organic vapours as dry fluids. The relevant differences are fluid molecular properties, reduced inlet state, specific head, volume flow and scale. Water may require wet-steam treatment; some ORC expansions may approach or enter a two-phase region. Few stages are often attractive because of specific head and economics, but multistage ORC machines are also established. This slide qualifies broad statements rather than introducing a new universal categorisation.

## Slide 10
ECONOMICS AND SCALE
Small-scale ORC is our focus today, but that is far from the whole ORC market
F10
KCORC 2026 | CTU UCEEB
1 kW
10 kW
100 kW
1 MW
10 MW
40 MW
Main teaching focus: tens to hundreds of kW
Small products
Tolerances, bearings, seals and conversion losses can dominate the engineering effort
Large installations
Commercial ORC systems extend to tens of MW; axial multi-stage choices remain relevant – typically in geothermal/biomass
Positive-displacement expanders are another popular option at small power, especially sub 50 kW.
Notes: The axis is an illustrative scope map, not a histogram or a claim about sales distribution. The thesis concentrates on small-scale turboexpanders. A current manufacturer example, Turboden, states products up to 40 MWe per shaft; this corrects a possible impression that ORC machines stop at the MW scale. Do not infer all ORC turbines are high speed or single stage. The turbine-versus-positive-displacement decision also depends on volume flow, pressure ratio, fluid, operating hours and cost.

## Slide 11
BLADE-ROW FUNDAMENTALS
Impulse or reaction- where is the static enthalpy drop?
F12
KCORC 2026 | CTU UCEEB
Static pressure (schematic)
Stator
Rotor
Impulse limit
Reaction
Impulse stage
Most expansion occurs in the stator; the rotor mainly turns the jet.
Reaction stage
Part of the static enthalpy drop occurs inside the rotor.
Notes: The sketch shows idealised pressure distributions, not an exact measured expansion. At constant radius, rothalpy conservation gives h1+w1^2/2=h2+w2^2/2 for an adiabatic rotor. In an impulse rotor with approximately constant static pressure, loss-induced reduction of relative speed can correspond to a static enthalpy rise. It must not be interpreted as a useful positive rotor expansion. Reaction is defined using a static enthalpy drop with an explicitly stated denominator. This is an intentional clarification of a potentially confusing earlier discussion.

## Slide 12: Impulse or reaction?

## Slide 13: Why a simple axial impulse turbine for small scale? Impulse versus Reaction Stage
uopt,impulse = uopt,reaction /
= *-*
Notes: In principle, any axial or radial turbine can be implemented as impulse or reaction stage.
In the case on an I stage the entire stage enthalpy drop or pressure drop is converted into kinetic energy within the nozzle row. Therefore, very high (supersonic) velocties are achieved wich reduce efficiency. The pressure and velocity across the rotor remain constant. Thus, no axial thrust is generated, partial admission is an option for part load and facilitates the realization of smaller turbines. This is further supported by the fact that even rotor inlet is subjected to the minimal pressure an maximal volume flow which occur in the cycle which helps to keep the blade height above a critical value.
In a R stage the enthalpy drop is equally distributed between nozzle and rotor blades. Thus, velocities are smaller and hence efficiency higher. Because there is a pressure drop across the rotor it produces axial thrust and partial admission does not work properly. Rotor inlet Ma are limited below unity – let´s say 0.85. This fact limits the achievable VRAT or PR below about 10.
Applying the EULER equation on both stages we can see that the possible specific work done in an I stage is 2u2 and in an R stage only 1u2. That means for the same specific work done, the i stage requires a about 30% lower circumferntial or rotational speed tha the R-stage.

## Slide 14
BLADE-ROW FUNDAMENTALS
Velocity triangles - a visual aid for a change of reference frame
F15
KCORC 2026 | CTU UCEEB
w1
c1
U
STATOR EXIT / ROTOR INLET
w2
c2
U
ROTOR EXIT
Absolute nozzle Mach: 1.49
Relative rotor inlet Mach: 0.81
Notes: The vectors use the uploaded R1233zd(E) case at 10000 rpm, D=0.2 m and both metal-angle inputs 27 degrees. Axial velocities are approximately 44 and 40 m/s. U=104.72 m/s. Inlet relative speed is 119.61 m/s, whereas nozzle absolute speed is 220.39 m/s. Divide each by the same inlet-to-rotor sound speed, 147.93 m/s, to obtain the distinct Mach numbers. Ask students to point to the reference frame associated with each arrow. Diagram is geometrically scaled from data, but row positions are illustrative.

## Slide 15
BLADE-ROW FUNDAMENTALS
The rotor extracts angular momentum
F16
KCORC 2026 | CTU UCEEB
General turbine Euler work
Axial stage at one mean radius
What high c2u tells us
Residual swirl is part of the exit kinetic energy. A diffuser or a following row may recover some of it.
What c2u does not tell us
Zero swirl is not automatically the efficiency optimum when other losses also change.
Notes: At fixed blade speed and inlet tangential velocity, Euler work increases as c2u decreases, including to negative c2u. Thus zero swirl is not the mathematical upper bound of Euler work. Exit kinetic energy depends on c2a as well as c2u. When changing speed or outlet metal angle, relative speed, incidence, rotor losses and exit kinetic energy vary together. This clarifies the earlier beta2 sweep: the nearest-to-zero point need not actually have zero swirl, and a constrained optimum is not a global optimum. General radial-machine work uses U1 and U2 separately.

## Slide 16
BLADE-ROW FUNDAMENTALS
Three ratios answer three different design questions
F17
KCORC 2026 | CTU UCEEB
Blade-speed ratio
„How fast is the blade relative to the available head?“
Flow coefficient
„How much axial flow passes relative to blade speed?“
Loading coefficient
„How much work does each stage extract?“
Notes: Separate these quantities explicitly because the early notebook called U/c_is a stage-loading indicator. That informal wording should not replace the conventional loading coefficient. Define c_is from the chosen total-to-static isentropic drop. The number of stages depends on the head that can be extracted per stage at acceptable velocity triangles, stress, Mach and efficiency. Similarity based on these ratios is useful but incomplete: Reynolds number, geometry ratios and real-fluid thermodynamic state also matter.

## Slide 17
BLADE-ROW FUNDAMENTALS
The metal stays fixed but the incoming flow angle moves
F18
KCORC 2026 | CTU UCEEB
Inlet: incidence
Changing rpm changes U.
That changes w1u and the inlet flow angle.
The blade leading edge does not rotate with it…
Outlet: deviation
The real flow need not leave at the metal angle.
Our simplified model sets outlet deviation to zero, in reality over/underloading…
Notes: In the supplied model the rotor loss fit assumes matched flow and metal angles. Keep its geometric turning definition; do not quietly replace it with arbitrary off-design flow turning. The added sin-squared incidence penalty with K_i=1 is an illustrative uncalibrated teaching assumption, not a validated general turbine correlation. Zero outlet deviation is a second explicit simplification. Do not claim either approximation predicts stall, shocks or separation. Students should see the distinction between a model closure and a conservation law.

## Slide 18
ECONOMICS AND SCALE
Small blade spans make ordinary tolerances expensive
F19
KCORC 2026 | CTU UCEEB
High vapour density + small flow
→ small active flow area
h = 2 mm
gap / h = 10%
h = 20 mm
gap / h = 1%
Same illustrative tip gap: 0.20 mm
Watch the clearances, chord and aspect ratio and not just absolute millimetres
Notes: The two gap ratios are a purely geometric illustration, not predictions of 10% and 1% leakage loss. The two blade drawings are not at one geometric scale. A small inlet volume flow can create short axial blades, increasing relative tip clearance and endwall influence. Small turbines are not automatically low-Reynolds-number: high density can offset reduced chord. Evaluate Re=rho*w*c/mu and relative roughness. Manufacturing throat errors also alter swallowing capacity.

## Slide 19
ECONOMICS AND SCALE
Partial admission trades more span for unsteady losses
F20
KCORC 2026 | CTU UCEEB
Full admission
Partial admission
Filling and emptying of rotor passages
Ventilation loss in inactive sectors
Periodic forcing and blade fatigue
A full ring of rotor blades can still be partially admitted by the stator.
Notes: The admission fraction measures active circumferential extent, not the fraction of rotor blades manufactured. Explain the trade-off at fixed mass flow: less active arc demands more height if the other flow variables remain fixed. Real stage losses include sector entry/exit processes and windage, and blade loading becomes periodic. The existing research code contains approximate partial-admission closures; they should not be taught as universal laws. Full-admission geometry should be handled consistently when rounding blade/nozzle counts.

## Slide 20
ECONOMICS AND SCALE
Smaller diameter can mean higher speed
F21
Derived illustration at U = 104.7 m/s and shaft power = 100 kW
KCORC 2026 | CTU UCEEB
D = 0.20 m
10 000 rpm
95.5 Nm
D = 0.05 m
40 000 rpm
23.9 Nm
The smaller rotor asks for a different bearing, rotordynamic and electrical solution
Notes: This arithmetic illustration holds U and shaft power fixed and therefore is not a pair of optimised turbine designs. Four times smaller mean diameter implies four times higher rpm and one quarter of the torque. High speed is driven by matching blade-speed ratio at small diameter, not directly by a rule that every organic-fluid machine rotates quickly. Stress, critical speeds, thrust, balance quality, bearing losses and generator cooling must be checked independently. This is where an aerodynamic optimum encounters mechanical feasibility.

## Slide 21
MECHANICAL INTEGRATION
Bearings and containment are part of the turbine design
F23
KCORC 2026 | CTU UCEEB
Three bearing families
Rolling bearings: lubrication, life and fluid compatibility
Gas / working-fluid bearings: rotor dynamics and start-stop behaviour
Active magnetic bearings: controls and touchdown support
Notes: The image is a crop of the author-supplied thesis Figure 5.5, printed page 98, showing the Mark II assembly; no performance claims are inferred from the drawing. Do not confuse magnetic couplings with magnetic bearings. Literature examples show feasibility, not a universal preferred choice: Rosset et al. report an oil-free small ORC turbogenerator on gas-lubricated bearings, while Tanaka et al. describe a hermetic generator with magnetic bearings. Selection depends on loads, speed, fluid, temperature, start-stop duty and economics.

## Slide 22
MECHANICAL INTEGRATION
High-speed generator AC is not grid-frequency AC
F24
KCORC 2026 | CTU UCEEB
Turbine
PM generator
Rectifier
+ DC link
Inverter
Grid / load
1 pole pair at 40 000 rpm
→ 667 Hz electrical frequency
Alternative= gearbox → lower-speed generator
Notes: The frequency equation is a standard synchronous-machine kinematic relation. With two poles (one pole pair), 40000/60=666.7 Hz. Power electronics decouple variable generator frequency from the grid. Semiconductor switching frequency is a different engineering choice and should not be equated to shaft-frequency-derived AC. A gearbox avoids some high-speed generator requirements but adds components, lubrication and losses. The overall package must include electrical losses and cooling, not only turbine isentropic efficiency.

## Slide 23
REAL-FLUID AERODYNAMICS
Z, gamma and Gamma
F26
KCORC 2026 | CTU UCEEB
Compressibility factor
Departure from the ideal-gas p-rho-T relation.
Heat-capacity ratio
Caloric response; alone not enough to reconstruct real fluid aerodynamics
Fundamental derivative of Gas Dyn.
Sound-speed variation and nonlinear wave behaviour.
Notes: Use R_s for the specific gas constant to avoid confusing it with the universal molar constant. Z can be below or above one, depending on state; dense vapour should not be defined by Z<1 as a universal rule. For a calorically perfect ideal gas, Gamma=(gamma+1)/2>1. For a real fluid, gamma=c_p/c_v is not generally the isentropic exponent in a^2=gamma*p/rho. Each property answers a different question, and an accurate EOS derivative is needed.

## Slide 24
REAL-FLUID AERODYNAMICS
Gamma tells us how sound speed changes on an isentrope
F27
KCORC 2026 | CTU UCEEB
Gamma > 1
Density falls → sound speed falls
Classical wave family
0 < Gamma < 1
Density falls → sound speed rises
Non-ideal, still classical wave family
Gamma < 0
Unconventional shockwave structures
Non-classical / BZT regime
Notes: Derive the sign directly from the definition rather than asking students to memorise the table. During an ordinary stable single-phase isentropic expansion density decreases. Hence a increases if Gamma<1. The distinction between classical and non-classical wave dynamics is Gamma=0, not Gamma=1. For a lossy flow path, da also includes (partial a/partial s)_rho ds, so a measured sound-speed increase alone cannot uniquely diagnose Gamma. Gamma exactly equal to one gives a locally zero isentropic density derivative of a.

## Slide 25
REAL-FLUID AERODYNAMICS
The state path matters as much as the fluid
F28
KCORC 2026 | CTU UCEEB
MM: regions of Gamma < 1
Our R1233zd(E) isentrope
20 bar, 150 °C inlet
a = 128.4 m/s
a = 146.4 m/s
5 bar ideal outlet
14% net increase in sound speed.
Evaluate Gamma locally along the path.
Notes: The left-hand figure is reproduced from the author's thesis, Figure 2.8, showing MM and not R1233zd(E). Do not imply the pictured Gamma map belongs to the notebook fluid. The right-hand numbers are endpoints of the uploaded R1233zd(E) isentrope, with a 14.018% net increase. Only endpoint data are used here: they do not prove Gamma<1 everywhere along the interval. The notebook can evaluate Gamma locally. The figure is a property map, not a measured turbine performance map.

## Slide 26
NOZZLE DESIGN
A convergent-divergent nozzle does two different jobs
F30
KCORC 2026 | CTU UCEEB
Subsonic acceleration
Supersonic acceleration
Sonic throat
Throat area
Sets the choked flow capacity for a given inlet total state.
Divergent passage
Sets expansion and turning towards the target outlet flow.
Notes: The nozzle contour is an original qualitative sketch, not a manufacturing profile. In a standard steady adiabatic isentropic single-phase nozzle, dA/A=(Ma^2-1) dc/c. Geometry alone does not guarantee the flow regime: the inlet state and back pressure must support choking and the appropriate branch. Real-fluid sound speed and density enter the sonic state. Boundary layers, blockage, finite trailing-edge thickness and stator turning alter a practical passage. The meanline tool sizes areas; detailed geometry remains another level of modelling.

## Slide 27
NOZZLE DESIGN
Use the real fluid isentrope to size and shape the passage
F31
KCORC 2026 | CTU UCEEB
1
Inlet total state
h0 and s0
2
Pressure sweep
h(p,s0), rho(p,s0), a(p,s0)
3
Sonic state
Find c(p*) = a(p*)
4
Areas + contour
Capacity, expansion, turning
Notes: Keep h0 and s0 distinct from static properties. The first ordinary sonic point satisfies h0-h*=a*^2/2. The formula uses total active throat area, not full annulus area. For the actual outlet, use the selected loss model and matching density and velocity. Method of characteristics provides an inviscid contour in the supersonic region; a boundary-layer correction and CFD/experiment are separate. Uniform geometric scaling preserves area ratio. Stretching a contour to force a different outlet ratio is a new aerodynamic shape requiring verification, not a correction that preserves the original MOC solution.

## Slide 28
NOZZLE DESIGN
The same nozzle cannot be perfectly adapted at every back pressure
F32
KCORC 2026 | CTU UCEEB
Adapted
p_exit = p_back
Underexpanded
p_exit > p_back
Overexpanded
p_exit < p_back
Notes: The three sketches indicate wave tendencies downstream of a supersonic nozzle; they are not complete flow solutions. Overexpanded operation may develop shocks and separation, including inside the passage depending on back pressure. Choked capacity is independent of further downstream-pressure reduction only while the choked regime and inlet total state are maintained. There is no universal real-fluid critical ratio of 0.52-0.60. The current teaching off-design model monitors outlet-area mismatch, but does not resolve these wave structures. Therefore it should be presented as a reduced model, especially far from design.

## Slide 29
MODEL CREDIBILITY
A great 1D meanline design may become into a terrible hardware
F34
KCORC 2026 | CTU UCEEB
EOS
Check state and derivatives
Meanline
Size and compare concepts
MOC / 2D
Shape supersonic passages
CFD
Resolve relevant flow losses
Experiment
Test the complete hardware
A model predicts useful trends.
It does not certify a nozzle, bearing system, rotor stress limit or guaranteed efficiency…
Notes: The prototype discussion in the thesis explicitly identifies model limitations: radial variations, boundary layers, mechanical losses, diffuser uncertainty and manufacturing effects. An optimisation can exploit an empirical model outside its evidence base. A positive result with a small conservation residual only confirms internal consistency, not hardware accuracy. NICFD still needs reliable property measurements/EOS validation. This is the key bridge to a responsible hands-on tutorial: students should explain both the result and what the model does not contain.

## Slide 30: One way to reduce Design uncertainty: High fidelity CFD Numerical simulation
Geometry consists of two computational domains S and R
  Domain S contains 2 stator blade channels (Laval nozzles)
  The rotating domain R contains 7 intermediate blade channels.
  Both domains have the same tangential pitch of 2π/5
  Connected with frozen rotor interface
SST k-ω turbulence model
Pressure inlet BC with total p and total T given
Pressure outlet BC with static p given

## Slide 31: High fidelity CFD Numerical simulation

## Slide 32
BLOCK D
Blade-to-blade plane design and notation
Notes: Separate aerodynamic losses embedded in velocity coefficients from explicit mechanical/ventilation losses. The bar chart is a model bookkeeping aid, not a full exergy balance. [Sources] - design_point.json — power and loss values. - correlations.py — disk-friction and partial-admission loss models. - model.py — efficiency calculation. [/Sources]

## Slide 33
BLOCK D
Meridional plane design and notation
Notes: Separate aerodynamic losses embedded in velocity coefficients from explicit mechanical/ventilation losses. The bar chart is a model bookkeeping aid, not a full exergy balance. [Sources] - design_point.json — power and loss values. - correlations.py — disk-friction and partial-admission loss models. - model.py — efficiency calculation. [/Sources]

## Slide 34
BRIDGE TO TESPY
One turbine model and three things to pass to the cycle
F37
KCORC 2026 | CTU UCEEB
Efficiency
A reduced curve along an assumed optimal-speed line.
Mass-flow capacity
Evaluate from the current turbine inlet total state.
Speed information
Report the associated rpm; do not solve it as a cycle input.
Notes: The reduced efficiency curve is calibrated along the selected fixed-outlet-pressure and inlet-superheat trajectory for one fluid and one frozen machine. Using it elsewhere is an approximation that must be stated, not made universal by normalisation. In TESPy the actual mass-flow residual should use the fixed throat and the current total inlet state, or negligible approach velocity. If a valve is introduced, use its downstream state. The root condition is h0-h*=a*^2/2 on s=s0, and the component residual is m_dot_TESPy-Cd*Astar*rhostar*astar=0. Check the valid choked operating region.

## Slide 35
ORC turbine design
Download KCORC_summer_school.zip
Extract KCORC_summer_school.zip
Double-click START_KCORC.bat
Wait until JupyterLab opens in your browser
Open: ORC_turbo_design/01_supersonic_orc_turbine_completed.ipynb
Run cells with Shift + Enter
No Python installation or IDE setup is required.
Notes: J01 - ORC turbine design: guided Jupyter workshop Suggested pace: 1 minute. This replaces the older notebook companion deck, not the foundations lecture. The class has already discussed turbomachinery physics before coffee. Use these slides as signposts, task prompts and joint checkpoints; spend most of the 100 minutes in the notebook. No previous Python experience is assumed. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 36
START HERE
RUN IN NOTEBOOK
Open the guided notebook and run the first cells
J04
KCORC 2026 | CTU UCEEB
IN THE FILE BROWSER
01_supersonic_orc_turbine_
completed.ipynb
default_inputs = DesignInputs(...)
design_explorer(default_inputs)
Before changing anything
Run imports first.
Run the prepared input cell.
Confirm one working explorer.
Notes: J04 - Open the guided notebook and run the first cells Suggested pace: 4 minutes. Open 01_supersonic_orc_turbine_student_guided.ipynb in the prepared Summer School JupyterLab environment. Run the imports, then the prepared DesignInputs cell, then design_explorer(default_inputs). This slide deliberately does not introduce a second environment-installation procedure. Important source-code behaviour: the widget calls replace(default, ...), so moving its sliders does not overwrite default_inputs, inputs or an already calculated reference_design. It is a preview. Later work uses the explicit baseline inputs cell. If startup fails, assist locally or let the pair share a machine; do not turn this into an installation workshop. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied widgets.py and the later image-widget version discussed in the conversation. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 37
REFERENCE CASE
LOOK & PREDICT
Everyone starts from the same saved design point
J05
KCORC 2026 | CTU UCEEB
Working fluid
R1233zd(E)
Pure fluid, real-property backend
Inlet
20 bar
150 °C
Outlet
5 bar
Static back pressure
Design mass flow
5.025
kg/s
Rotor speed
10 000
rpm
Mean diameter
0.200
m
Notes: J05 - Everyone starts from the same saved design point Suggested pace: 2 minutes. These are prescribed design inputs, not free off-design inputs. Describe p_in and T_in as inlet total quantities under the negligible approach-velocity convention in the notebook; p_out is static. Keep the baseline unchanged until after the equation exercises. Requested full admission is 1.0; the current source model rounds the nozzle count and stores an effective value 0.994718. Do not silently replace the model output with exact unity. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 38
EQUATION → PYTHON 1
TRY IN NOTEBOOK
A — Turn the cycle conditions into a velocity scale
J06
KCORC 2026 | CTU UCEEB
Your five outputs
Pressure ratio
Isentropic head and velocity
Blade speed and U/c_is
Notes: J06 - A — Turn the cycle conditions into a velocity scale ACTIVITY 1 | 6 minutes. Notebook location: Block A - From cycle conditions to stage loading. Leave this slide projected while pairs work. Ask them to say what the equation means before editing. Only the marked np.nan expressions are editable. Do not ask them to write a function, loop or a property call. A syntax problem does not block the next section: the guided notebook uses the reference model downstream. Advance to the checkpoint only when discussing together. Suggested solution (not shown to participants yet): student_pressure_ratio = inputs.p_in_Pa / inputs.p_out_Pa student_dh_is_J_kg = state_in["h_J_kg"] - state_out_is["h_J_kg"] student_c_is_m_s = np.sqrt(2.0 * student_dh_is_J_kg) student_U_m_s = np.pi * inputs.D_mid_m * inputs.n_rpm / 60.0 student_U_over_cis = student_U_m_s / student_c_is_m_s Discussion prompt: What happens to U/c_is if n doubles while the inlet state, outlet pressure and diameter stay fixed? [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 39
REFERENCE CHECKPOINT
CHECK TOGETHER
A — Check the scale before trusting the next calculation
J07
KCORC 2026 | CTU UCEEB
Pressure ratio
4.00
p_in / p_out
Isentropic head
28.83
kJ/kg
Isentropic velocity
240.1
m/s
Blade speed
104.7
m/s
Blade-speed ratio
0.436
U/c_is
Notes: J07 - A — Check the scale before trusting the next calculation Suggested pace: 3 minutes after the activity. Expected values are pressure ratio 4; dh_is 28830.3958 J/kg; c_is 240.1266 m/s; U 104.7198 m/s; U/c_is 0.436102. If velocity is about 7.6 m/s, ask whether enthalpy was used in kJ/kg instead of J/kg. At fixed geometry and thermodynamic boundary conditions, doubling speed doubles U/c_is, not the imposed pressure ratio. Refer to this quantity as blade-speed ratio; the foundations deck distinguishes it from the conventional loading coefficient. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 40
EQUATION → PYTHON 2
TRY IN NOTEBOOK
B — Will the ideal nozzle outlet be supersonic?
J08
KCORC 2026 | CTU UCEEB
Inlet enthalpy
504 812
J/kg
Ideal outlet enthalpy
475 982
J/kg
Outlet sound speed
146.39
m/s
Notes: J08 - B — Will the ideal nozzle outlet be supersonic? ACTIVITY 2 | 4 minutes. Notebook location: Block B - Supersonic stator and sonic throat. Leave this slide projected while pairs work. Ask them to say what the equation means before editing. Only the marked np.nan expressions are editable. Do not ask them to write a function, loop or a property call. A syntax problem does not block the next section: the guided notebook uses the reference model downstream. Advance to the checkpoint only when discussing together. Suggested solution (not shown to participants yet): student_c_exit_is_m_s = np.sqrt(2.0 * (h_in_J_kg - h_out_is_J_kg)) student_Ma_exit_is = student_c_exit_is_m_s / a_out_is_m_s Discussion prompt: Before calculating: compare the velocity scale from Block A with the real-fluid outlet sound speed. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 41
REFERENCE CHECKPOINT
CHECK TOGETHER
B — A sonic throat connects the inlet to a supersonic outlet
J09
KCORC 2026 | CTU UCEEB
RUN THE PROVIDED PRESSURE-PATH CELL
Ma < 1
Ma = 1
Ma > 1
Sonic pressure
1.248
MPa
Ideal outlet Mach
1.640
-
The model finds the sonic state from the real fluid isentrope, not a fixed ideal-gas pressure ratio.
Notes: J09 - B — A sonic throat connects the inlet to a supersonic outlet Suggested pace: 3 minutes. Run the supplied path cell. The line art on this slide is schematic, not a MOC contour or a nozzle-coordinate export. The sonic pressure comes from the saved reference model: 1.247649 MPa. The reference design samples the first Ma>=1 point in its pressure grid; do not claim this is an exact root-finding solution. The student's two scalar equations confirm c_is=240.13 m/s and Ma_exit,is=1.6403. No student has to implement the pressure loop. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 42
BLOCK B
Quasi-1D nozzle path and choking
12
KCORC Summer School 2026
convergent
throat
divergent
Notes: Walk through the pressure sweep: at each pressure, the static state comes from the inlet entropy, then enthalpy converts into kinetic energy. The first Ma≥1 point identifies the throat. [Sources] - model.py — _isentropic_path() and throat identification. - design_point.json — p_throat and Ma_out_is. [/Sources]

## Slide 43
SUPPLIED LOSS MODEL
RUN ONLY
B — A real nozzle converts less of the head into jet speed
J11
KCORC 2026 | CTU UCEEB
Nozzle coefficient
0.918
phi_s
Loss-adjusted velocity
220.4
m/s
Loss-adjusted Mach
1.490
-
The empirical coefficient is provided. There are many other options to account for losses
Notes: J11 - B — A real nozzle converts less of the head into jet speed Suggested pace: 2 minutes. Do not ask participants to reproduce polynomial coefficients. In the supplied model phi_s=0.917810, c1=220.3907 m/s and Ma1=1.489838. h1=480525.924 J/kg exceeds the isentropic outlet enthalpy. The actual outlet sound speed also changes, so Ma1 is not simply phi_s times the ideal Mach. Use the outlet formula shown; the path implementation has its own pedagogical loss distribution and is not re-derived here. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 44
BLOCK B
Full nozzle geometric design – method of characteristics
12
KCORC Summer School 2026
Notes: Walk through the pressure sweep: at each pressure, the static state comes from the inlet entropy, then enthalpy converts into kinetic energy. The first Ma≥1 point identifies the throat. [Sources] - model.py — _isentropic_path() and throat identification. - design_point.json — p_throat and Ma_out_is. [/Sources]

## Slide 45
EQUATION → PYTHON 3
TRY IN NOTEBOOK
B — Use continuity twice to size the nozzle
J12
Notebook: Continuity and nozzle area | three EDIT HERE expressions
KCORC 2026 | CTU UCEEB
At the throat
Use rho_star_kg_m3
and c_star_m_s.
At the outlet
Use the loss-adjusted
density and velocity.
Both areas are normal to the local flow. Calculate their ratio only after calculating each area.
Notes: J12 - B — Use continuity twice to size the nozzle ACTIVITY 3 | 5 minutes. Notebook location: Block B - Continuity and nozzle area. Leave this slide projected while pairs work. Ask them to say what the equation means before editing. Only the marked np.nan expressions are editable. Do not ask them to write a function, loop or a property call. A syntax problem does not block the next section: the guided notebook uses the reference model downstream. Advance to the checkpoint only when discussing together. Suggested solution (not shown to participants yet): student_A_throat_m2 = inputs.m_dot_kg_s / (rho_star_kg_m3 * c_star_m_s) student_A_outlet_m2 = inputs.m_dot_kg_s / (rho_nozzle_out_kg_m3 * c_nozzle_out_m_s) student_area_ratio = student_A_outlet_m2 / student_A_throat_m2 Discussion prompt: Which density and velocity belong to each section? Are these total areas for all nozzles, or one slot? [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 46
JOINT INTERPRETATION
CHECK TOGETHER
B — Choose the velocity normal to the area you use
J14
KCORC 2026 | CTU UCEEB
Flow-normal nozzle section
The normal follows the jet.
Use c₁ = 220.4 m/s.
Axial annulus plane
The normal follows the axis.
Use c₁a = 43.94 m/s.
Same continuity equation. Different surface orientation. No conflict between the two calculations.
Notes: J14 - B — Choose the velocity normal to the area you use Suggested pace: 3 minutes. This applies the control-surface distinction already introduced in the foundations lecture. No need for a new coding task. For a section normal to the local nozzle velocity use c1=220.3907 m/s. For the axial annulus plane use c1a=43.93884 m/s because alpha1=11.5 deg is measured from the tangential direction. Then A_axial=e*pi*D*h=A_normal/sin(alpha1); using either consistently yields the same mass flow. Blockage and nonuniformity are neglected in this first-order construction. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 47
EQUATION → PYTHON 4A
TRY IN NOTEBOOK
C — Step into the moving rotor frame
J15
KCORC 2026 | CTU UCEEB
Angle hint
Use arctan2(axial, tangential),
then convert radians to degrees.
The first velocity line is done.
Notes: J15 - C — Step into the moving rotor frame ACTIVITY 4A | 7 minutes. Notebook location: Block C - Rotor velocity triangle, metal angle, and incidence. Leave this slide projected while pairs work. Ask them to say what the equation means before editing. Only the marked np.nan expressions are editable. Do not ask them to write a function, loop or a property call. A syntax problem does not block the next section: the guided notebook uses the reference model downstream. Advance to the checkpoint only when discussing together. Suggested solution (not shown to participants yet): student_w1a_m_s = c1a_m_s # already completed student_w1u_m_s = c1u_m_s - U_m_s student_w1_m_s = np.hypot(student_w1a_m_s, student_w1u_m_s) student_beta1_flow_deg = np.degrees(np.arctan2(student_w1a_m_s, student_w1u_m_s)) student_incidence_deg = student_beta1_flow_deg - inputs.beta_rotor_in_deg Discussion prompt: Does the blade metal angle change when speed changes? Which component is altered by subtracting U? [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 48
SUPPLIED ROTOR MODEL
RUN ONLY
C — Keep the metal angle; account for incidence separately
J17
KCORC 2026 | CTU UCEEB
Zero-incidence coefficient
0.777
after the height correction
Effective coefficient
0.771
including inlet incidence
Outlet assumption
Flow follows metal.
Deviation is neglected.
27° outlet-angle input = 153° direction from +u
Notes: J17 - C — Keep the metal angle; account for incidence separately Suggested pace: 3 minutes. The empirical matched-flow coefficient is evaluated using geometric turning. The teaching addition uses phi_eff^2=phi_0^2-K_i*sin(i)^2 with K_i=1. This is a transparent low-order assumption, not a validated universal incidence correlation. Do not present it as a result of the original design correlation. The saved height-corrected zero-incidence coefficient is 0.776973 and the effective coefficient is 0.771152. The outlet slider 27 deg denotes an acute angle from -u, so its direction measured from +u is 153 deg. Outlet deviation is neglected in this model. No student edits on this slide. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 49
EQUATION → PYTHON 4B
TRY IN NOTEBOOK
D — One line turns angular momentum into power
J18
KCORC 2026 | CTU UCEEB
Mass flow
5.025
kg/s
Blade speed
104.7
m/s
Tangential change
190.1
m/s
Notes: J18 - D — One line turns angular momentum into power ACTIVITY 4B | 4 minutes. Notebook location: Block D - Euler work, losses, and turbine efficiency. Leave this slide projected while pairs work. Ask them to say what the equation means before editing. Only the marked np.nan expressions are editable. Do not ask them to write a function, loop or a property call. A syntax problem does not block the next section: the guided notebook uses the reference model downstream. Advance to the checkpoint only when discussing together. Suggested solution (not shown to participants yet): student_P_aero_W = inputs.m_dot_kg_s * U_m_s * (c1u_m_s - c2u_m_s) Discussion prompt: Should this turbine produce tens of watts, kilowatts, or megawatts? What sign should turbine power have? [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 50
REFERENCE CHECKPOINT
CHECK TOGETHER
D — Separate aerodynamic, shaft and electrical power
J19
KCORC 2026 | CTU UCEEB
Aerodynamic power
100.05
kW
Mechanical power
99.68
kW
Total-to-static efficiency
0.688
P_mech / (m_dot * dh_is)
Disk friction: 0.337 kW
Partial-admission term: 0.028 kW
Notes: J19 - D — Separate aerodynamic, shaft and electrical power Suggested pace: 4 minutes. The supplied model gives Paero=100047.235 W, disk friction=336.585 W, partial-admission loss=27.882 W, Pmech=99682.768 W and eta=0.688071. The small losses shown between Paero and Pmech do not mean the turbine is nearly 100 percent efficient: nozzle, rotor and residual-exit-velocity effects already enter Paero. Do not subtract aerodynamic losses again. Pmech is not a complete net electrical output. The input partial admission was 1.0 but the rounded source geometry gave 0.994718, explaining the nonzero small PA term. These values reproduce the source model, not a correction of it. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 51
GEOMETRY SUMMARY
LOOK & INTERPRET
D — Read the output as a first-order machine
J20
KCORC 2026 | CTU UCEEB
RADIAL SPAN VS. DIAMETER
h
hub
tip
mean
Mean diameter
200.0 mm
Rotor hub / tip
191.7 / 208.3 mm
Rotor height
8.25 mm
Stator / rotor count
24 / 25
Effective admission
0.995
A meanline design gives flow states and first order dimensions
Notes: J20 - D — Read the output as a first-order machine Suggested pace: 3 minutes. The nozzle height is 7.954984 mm and rotor height 8.254984 mm. The added 0.3 mm is a model height allowance, not a specified tip clearance. Dhub=Dmid-h and Dtip=Dmid+h. There are 24 stator nozzles and 25 rotor blades in the saved case. Effective admission is 0.994718 after rounding. The unrolled meridional sketch is conceptual and not to scale; do not use it as a CAD section. Participants should compare the same values in reference_design.summary(). [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 52
PAIRED ENGINEERING EXPERIMENT
TRY IN NOTEBOOK
Change one input; predict two consequences
J21
KCORC 2026 | CTU UCEEB
01 Shaft speed
Change n.
Watch U/c_is and incidence.
What happens to power?
02 Inlet metal angle
Change beta1.
Compare metal and flow.
Watch the rotor coefficient.
03 Outlet metal angle
Change beta2.
Watch c2u and efficiency.
Does zero swirl appear?
Choose one case. Record the baseline. Make one change. Explain the trade-off.
Notes: J21 - Change one input; predict two consequences Suggested pace: 8-10 minutes. Each pair chooses just one case and records a baseline and a changed point. Speed case: change rpm, keep the other widgets fixed and watch blade-speed ratio, incidence, exit swirl and efficiency. Incidence case: change beta1 metal toward beta1 flow; explain that the design explorer also changes geometric turning when beta1 changes, so it is not a pure isolated incidence experiment. Outlet-angle case: change beta2, watch phi_r, c2u and power; positive residual swirl is not evidence by itself of an optimiser failure. The explorer calls design_stage, so geometry may be re-sized when a sizing-related input changes; this is a design comparison, not automatically off-design of the same hardware. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 53
REDUCED OFF-DESIGN
RUN ONLY
E — Freeze the geometry before creating the handoff
J23
KCORC 2026 | CTU UCEEB
Hardware stays fixed
A*, A_out, diameter and height
Pitch, blade counts and metal angles
Operating state can change
Inlet state and pressure ratio
Mass flow, flow angle and best speed
Notes: J23 - E — Freeze the geometry before creating the handoff Suggested pace: 2 minutes. Move from design_stage to freeze_geometry(reference_design). The fixed geometry includes diameters, areas, heights, pitch, nozzle/blade counts and metal angles. The evaluation sweeps inlet pressure at fixed outlet pressure, preserves design superheat where available, and tests speeds internally. The exported one-dimensional efficiency characteristic uses the best sampled speed at each pressure ratio. The speed is informative but the curve still assumes ideal variable-speed control. If a maximum occurs at the search boundary it is only the best tested speed, not a demonstrated global optimum. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied turbine_reduced_characteristic.json, schema kcorc_reduced_turbine_characteristic_v1. Fixed outlet pressure 500000 Pa; inlet superheat preserved along the pressure sweep; efficiency-maximising speed selected internally; fixed choked throat with Cd=1. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx, relevant foundations slides; KCORC_2026_Supersonic_ORC_Turbine_Tutorial.pptx; supplied teaching source model.py, offdesign.py, correlations.py and incidence/NICFD additions discussed in the conversation. These are teaching-model assumptions, not independently validated universal correlations. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 54
REDUCED CHARACTERISTIC
LOOK & INTERPRET
E — Give TESPy one efficiency curve
J24
KCORC 2026 | CTU UCEEB
0.67
0.69
0.71
0.73
0.75
2
3
4
5
6
design
Pressure ratio [-]
Efficiency [-]
One cycle input
Interpolate eta(PR).
Optimal rpm is reported,
not prescribed as a
second map coordinate.
The curve assumes ideal variable speed operation along one specified thermodynamic path.
Notes: J24 - E — Give TESPy one efficiency curve Suggested pace: 3 minutes. Curve points are redrawn from the supplied JSON, not re-simulated. Thirty samples span PR=1.8 to 6.1032258. The ideal variable-speed speed sweep is internal, so shaft rpm is not a second independent axis in the handoff. The saved reference design at PR=4 and 10000 rpm has eta=0.688071; the optimal-speed curve is about 0.6909 at PR=4, so it need not pass through that efficiency value. Do not imply global validation from smoothness. In the previous diagnostics, the stator correlation and neglected off-design matching physics affected this decreasing trend. The 1D reduction belongs to the saved inlet-state path and fluid, not every ORC with the same pressure ratio. [Sources] Author-supplied turbine_reduced_characteristic.json, schema kcorc_reduced_turbine_characteristic_v1. Fixed outlet pressure 500000 Pa; inlet superheat preserved along the pressure sweep; efficiency-maximising speed selected internally; fixed choked throat with Cd=1. Author-supplied design_point.json: R1233zd(E), inlet 2 MPa / 423.15 K, outlet 0.5 MPa, 5.025 kg/s, 10000 rpm, mean diameter 0.2 m, inlet/outlet rotor metal-angle inputs 27 deg. Numbers are saved model outputs, not measured performance or a new solver run. Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 55
TURBINE SWALLOWING CAPACITY
LOOK & INTERPRET
E — Choked does not mean constant mass flow
J25
KCORC 2026 | CTU UCEEB
0
2
4
6
8
10
15
20
25
30
design
Turbine inlet pressure [bar]
Mass flow [kg/s]
TESPy must use
The current inlet state
and the fixed total
throat area.
Notes: J25 - E — Choked does not mean constant mass flow Suggested pace: 3 minutes. This plot uses inlet pressure, not pressure ratio, on the horizontal axis. All plotted points belong to the supplied sliding-pressure path with fixed outlet pressure and changing inlet temperature. Choking removes sensitivity to a further downstream-pressure reduction at a fixed inlet total state; it does not remove inlet-state sensitivity. m_dot=Cd*A_star*rho_star*a_star. For the TESPy residual, the sonic state must be evaluated from the current turbine inlet state; after an inlet control valve use the post-valve inlet. The JSON mass-flow array is a reference path, not a universal m_dot(PR) law. Outside the choked regime a separate model is needed. [Sources] Author-supplied turbine_reduced_characteristic.json, schema kcorc_reduced_turbine_characteristic_v1. Fixed outlet pressure 500000 Pa; inlet superheat preserved along the pressure sweep; efficiency-maximising speed selected internally; fixed choked throat with Cd=1. Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied correspondence with Francesco Witte and the agreed sonic-throat residual pseudocode. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 56
EXPORT AND HANDOFF
RUN IN NOTEBOOK
E —JSON connects the two workshops
J26
KCORC 2026 | CTU UCEEB
"fluid": "R1233zd(E)"
"fixed_geometry": { "A_throat_m2": ... }
"mass_flow_model": {
"discharge_coefficient": 1.0
}
"characteristic": {
"pressure_ratio": [...],
"eta_is_ts": [...],
"n_opt_rpm": [...]
}
Today
Run the export cell.
Tomorrow
Use the file in
Francesco’s TESPY model.
Save outputs/turbine_reduced_characteristic.json. The turbine and cycle remain separate models.
Notes: J26 - E — One JSON connects the two workshops Suggested pace: 2 minutes. Run the export cell. The code block here is a schema illustration, not literal runnable JSON. Keep the filename turbine_reduced_characteristic.json. In the supplied schema the total throat area is in fixed_geometry and Cd is in mass_flow_model; the same data need not be duplicated. Wednesday's model should interpolate efficiency, evaluate the inlet-state-dependent choked mass-flow residual and report rpm for information. P_mech and tabulated mass flow are reference-path outputs and should not be treated as universal cycle outputs. Do not ask students to implement TESPy UDEs during Tuesday's session. [Sources] Author-supplied guided student notebook (01_supersonic_orc_turbine_student_guided.ipynb), as provided in this conversation. Section headings and student variable names are retained; no notebook code is changed by this deck. Author-supplied turbine_reduced_characteristic.json, schema kcorc_reduced_turbine_characteristic_v1. Fixed outlet pressure 500000 Pa; inlet superheat preserved along the pressure sweep; efficiency-maximising speed selected internally; fixed choked throat with Cd=1. Author-supplied spale2026_turbine_tespy.py and correspondence with Francesco Witte: separation of efficiency and mass-flow constraints. Author-supplied ORC_Turbomachinery_Fundamentals_Addon_EN.pptx and UCEEB_prezentace_vzor_022026_CZ.pptx: reuse of UCEEB logo and cover background; same Arial typography, CTU blue, teal panels, margins and footer language. [/Sources]

## Slide 57
Thank you!
Jan Špale, Ph.D.
jan.spale@cvut.cz
www.uceeb.cz
Notes: End the lecture portion here. Keep the final slide visible during questions and the transition back to JupyterLab. [Sources] - UCEEB_prezentace_vzor_022026_CZ.pptx — visual template and closing-slide style. [/Sources]